## Slide 1
MADE BY MATT / GROW SCIENCE
Levers, pulleys and gears
AUTUMN 1 · WEEK 4 · LESSON A
01
Change the force.
Notice the trade-off.
Name mechanisms, find a pivot and explain a gain and a cost.
Notes: Title — 1 minutes within the source's 40-minute lesson.
Introduce source learning intention. A mechanism may change force size, direction or both; a fixed pulley need not reduce force. The lesson explores the source's force-distance idea without claiming energy is created. Monday stops after We Do 2.
[Sources]
https://github.com/MattRoper1977/Lessons/blob/main/Science_Teesside/Grow/SCI_G_W4_Mechanisms.html
Git blob: 8aa3e1f001c3d3c944207d4eb44b93b1df4d7e46.
SHA256: a2d4bd4b2ec87aace94167b285bd1724bb9e2907f86a472b74b84fa48ffa53a0.
[/Sources]
[Sources] Generated contextual illustration for this visual edition; not measured or recorded experimental evidence. [/Sources]

## Slide 2
MADE BY MATT / GROW SCIENCE
Find the turning point
AUTUMN 1 · WEEK 4 · LESSON A
02
Supported: point to where scissors turn.
Standard: name that turning point.
Stretch: find it on a wheelbarrow drawing too.
Look, point, describe or draw.
01
02
03
Notes: Arrival Task — 3 minutes within the source's 40-minute lesson.
Source arrival task adapted for safe access: blunt scissors adult-approved or a drawing, no cutting task. Answer: scissors pivot is the screw/joint; wheelbarrow lever pivot is wheel axle. Wheelbarrow example can be drawn on board, no publisher image required. Never handle sharp blades to point. Use the next slide for the wheelbarrow drawing and one-minute check within this same Arrival stage.
[Sources]
https://github.com/MattRoper1977/Lessons/blob/main/Science_Teesside/Grow/SCI_G_W4_Mechanisms.html
Git blob: 8aa3e1f001c3d3c944207d4eb44b93b1df4d7e46.
SHA256: a2d4bd4b2ec87aace94167b285bd1724bb9e2907f86a472b74b84fa48ffa53a0.
[/Sources]

## Slide 3
MADE BY MATT / GROW SCIENCE
Check the wheelbarrow’s pivot
AUTUMN 1 · WEEK 4 · LESSON A
03
LOAD IN TRAY
handles
PIVOT: wheel axle
The wheel axle is the turning point when you lift the handles.
A wheelbarrow is a lever. The load sits between pivot and effort.
Notes: Arrival Task — 1 minutes within the source's 40-minute lesson.
Final minute of source four-minute Arrival stage. Original editable schematic supplied as the wheelbarrow picture: the small amber centre of the wheel is its axle/pivot. Ask learner to locate the turning point before reading the explanation. Wheelbarrow is a second-class lever: load between wheel axle and effort at handles. Drawing is schematic, not a scale force diagram. No physical wheelbarrow or heavy load needed.
[Sources]
https://github.com/MattRoper1977/Lessons/blob/main/Science_Teesside/Grow/SCI_G_W4_Mechanisms.html
Git blob: 8aa3e1f001c3d3c944207d4eb44b93b1df4d7e46.
SHA256: a2d4bd4b2ec87aace94167b285bd1724bb9e2907f86a472b74b84fa48ffa53a0.
[/Sources]

## Slide 4
MADE BY MATT / GROW SCIENCE
Three things to notice
AUTUMN 1 · WEEK 4 · LESSON A
04
1 Find the pivot.
2 Move it and compare the effort.
3 Explain what you gain and what it costs.
Notes: Today at a Glance — 2 minutes within the source's 40-minute lesson.
Retain current source sequence. Agree response and sensory choices. Today's controlled adult demonstration prepares Tuesday's pupil/director comparison; don't count it as their independent practical.
[Sources]
https://github.com/MattRoper1977/Lessons/blob/main/Science_Teesside/Grow/SCI_G_W4_Mechanisms.html
Git blob: 8aa3e1f001c3d3c944207d4eb44b93b1df4d7e46.
SHA256: a2d4bd4b2ec87aace94167b285bd1724bb9e2907f86a472b74b84fa48ffa53a0.
[/Sources]

## Slide 5
MADE BY MATT / GROW SCIENCE
A lever turns about a pivot
AUTUMN 1 · WEEK 4 · LESSON A
05
EFFORT
LOAD
PIVOT
The effort pushes one end. The load rises at the other end.
The pivot is the turning point.
Notes: I Do 1 — 4 minutes within the source's 40-minute lesson.
First four minutes of source nine-minute I Do 1. Define lever: rigid bar rotating about pivot; mechanism changes force size or direction. Arrow diagram schematic only, not force magnitude. The little secured eraser is the load. Effort arm is distance pivot-to-effort; load arm pivot-to-load. No numerical calculations needed.
[Sources]
https://github.com/MattRoper1977/Lessons/blob/main/Science_Teesside/Grow/SCI_G_W4_Mechanisms.html
Git blob: 8aa3e1f001c3d3c944207d4eb44b93b1df4d7e46.
SHA256: a2d4bd4b2ec87aace94167b285bd1724bb9e2907f86a472b74b84fa48ffa53a0.
[/Sources]

## Slide 6
MADE BY MATT / GROW SCIENCE
Move the pivot, keep the load
AUTUMN 1 · WEEK 4 · LESSON A
06
Watch the adult use the middle pivot.
Predict what changes when it moves near the load.
Keep the effort point and small load rise the same.
Compare the effort and the hand’s travel.
01
02
03
04
Notes: I Do 1 — 5 minutes within the source's 40-minute lesson.
Completes source nine-minute demonstration. Adult-secured broad pivot, ruler/card lever and light secured load, small lift target; never launch objects, hands clear. Near-load pivot lengthens effort arm relative to load arm, reducing needed effort force ideally; for same load rise, effort end travels farther. Repeat both positions. Real friction/bending means report observations honestly. No kit: use lever sketch as explanation/prediction only.
[Sources]
https://github.com/MattRoper1977/Lessons/blob/main/Science_Teesside/Grow/SCI_G_W4_Mechanisms.html
Git blob: 8aa3e1f001c3d3c944207d4eb44b93b1df4d7e46.
SHA256: a2d4bd4b2ec87aace94167b285bd1724bb9e2907f86a472b74b84fa48ffa53a0.
[/Sources]

## Slide 7
MADE BY MATT / GROW SCIENCE
Which objects are levers?
AUTUMN 1 · WEEK 4 · LESSON A
07
Wheelbarrow
Scissors
Spanner on a bolt
Point to a turning point before naming it.
01
02
03
Notes: We Do 1 — 2 minutes within the source's 40-minute lesson.
First two of source ten-minute We Do 1. Wheelbarrow rotates around wheel axle; scissors are a pair of levers around joint; spanner turns around bolt axis. Name where effort is applied. Adult models the wheelbarrow using drawing rather than heavy equipment. Pointing, speech or annotations equally valid.
[Sources]
https://github.com/MattRoper1977/Lessons/blob/main/Science_Teesside/Grow/SCI_G_W4_Mechanisms.html
Git blob: 8aa3e1f001c3d3c944207d4eb44b93b1df4d7e46.
SHA256: a2d4bd4b2ec87aace94167b285bd1724bb9e2907f86a472b74b84fa48ffa53a0.
[/Sources]

## Slide 8
MADE BY MATT / GROW SCIENCE
A fixed pulley changes direction
AUTUMN 1 · WEEK 4 · LESSON A
08
At a flagpole, pull the rope down and the flag goes up.
One fixed pulley changes the pull’s direction. It does not give free lifting force.
pull down
load rises
Notes: We Do 1 — 3 minutes within the source's 40-minute lesson.
Next three minutes source We Do 1. Trace rope over fixed top wheel on board/native sketch. Ideal fixed pulley effort force is approximately load weight; real friction can increase it. This differs from a pulley system with more supporting rope sections. No pupil lifting, hanging or rope-around-body activity. Offline diagram fully substitutes animation.
[Sources]
https://github.com/MattRoper1977/Lessons/blob/main/Science_Teesside/Grow/SCI_G_W4_Mechanisms.html
Git blob: 8aa3e1f001c3d3c944207d4eb44b93b1df4d7e46.
SHA256: a2d4bd4b2ec87aace94167b285bd1724bb9e2907f86a472b74b84fa48ffa53a0.
[/Sources]

## Slide 9
MADE BY MATT / GROW SCIENCE
Gears trade speed for turning effect
AUTUMN 1 · WEEK 4 · LESSON A
09
Gears have teeth and pass on turning movement.
A bicycle uses chainrings, a chain and sprockets.
A lower gear can help turn the wheel against a load.
The wheel turns fewer times per pedal turn.
01
02
03
04
Notes: We Do 1 — 3 minutes within the source's 40-minute lesson.
Next three minutes of source We Do 1. Source everyday example 'bicycle chain and cogs' is a chain drive with gear ratios, not two directly meshing gears. Explain torque as turning effect in accessible words. With lower gearing, wheel torque is greater for comparable pedal torque but wheel speed per pedal turn is lower; rider must turn pedals more often for same distance. Keep fingers away from real moving gears. No ratio maths required.
[Sources]
https://github.com/MattRoper1977/Lessons/blob/main/Science_Teesside/Grow/SCI_G_W4_Mechanisms.html
Git blob: 8aa3e1f001c3d3c944207d4eb44b93b1df4d7e46.
SHA256: a2d4bd4b2ec87aace94167b285bd1724bb9e2907f86a472b74b84fa48ffa53a0.
[/Sources]

## Slide 10
MADE BY MATT / GROW SCIENCE
Check the mechanism and its job
AUTUMN 1 · WEEK 4 · LESSON A
10
MECHANISM
EVERYDAY EXAMPLE
Lever
Fixed pulley
Geared chain drive
Scissors, wheelbarrow, spanner
Flagpole rope over top wheel
Bicycle chain and cogs
Notes: We Do 1 — 2 minutes within the source's 40-minute lesson.
Final two minutes source We Do 1. Reveal after classification. Learner chooses one example and describes force or movement direction. Do not imply each example reduces force in every use; names alone do not establish a benefit. Correct one label with reason.
[Sources]
https://github.com/MattRoper1977/Lessons/blob/main/Science_Teesside/Grow/SCI_G_W4_Mechanisms.html
Git blob: 8aa3e1f001c3d3c944207d4eb44b93b1df4d7e46.
SHA256: a2d4bd4b2ec87aace94167b285bd1724bb9e2907f86a472b74b84fa48ffa53a0.
[/Sources]

## Slide 11
MADE BY MATT / GROW SCIENCE
Explain the gain and the cost
AUTUMN 1 · WEEK 4 · LESSON A
11
This is a ___ because ___. It helps by ___, but you have to ___.
Name the mechanism, its job and the trade-off.
Notes: I Do 2 — 4 minutes within the source's 40-minute lesson.
Exact four-minute I Do 2 evidence loop. Model lever: rigid bar about pivot; near-load pivot can need less effort force but hand travels farther for same load rise. Record named mechanisms, correctly identified pivot and gain/cost. Do not require photographs: labelled diagram and explanation suffice. Actual comparison evidence follows Tuesday.
[Sources]
https://github.com/MattRoper1977/Lessons/blob/main/Science_Teesside/Grow/SCI_G_W4_Mechanisms.html
Git blob: 8aa3e1f001c3d3c944207d4eb44b93b1df4d7e46.
SHA256: a2d4bd4b2ec87aace94167b285bd1724bb9e2907f86a472b74b84fa48ffa53a0.
[/Sources]

## Slide 12
MADE BY MATT / GROW SCIENCE
Sort the gain and the cost
AUTUMN 1 · WEEK 4 · LESSON A
12
Less effort force needed
Hand travels farther
Pull down instead of up
Mechanism creates extra energy
Slower turning, greater turning effect
01
02
03
04
05
Notes: We Do 2 — 5 minutes within the source's 40-minute lesson.
First five of source ten-minute We Do 2. Sort into GAIN, COST, NEITHER, or GAIN AND COST. Give an attempt before next slide. Explain intended task matters. 'Creates extra energy' is false, not a legitimate benefit. Spoken pointing or paper cards replace tap/drag controls.
[Sources]
https://github.com/MattRoper1977/Lessons/blob/main/Science_Teesside/Grow/SCI_G_W4_Mechanisms.html
Git blob: 8aa3e1f001c3d3c944207d4eb44b93b1df4d7e46.
SHA256: a2d4bd4b2ec87aace94167b285bd1724bb9e2907f86a472b74b84fa48ffa53a0.
[/Sources]

## Slide 13
MADE BY MATT / GROW SCIENCE
Check your choices
AUTUMN 1 · WEEK 4 · LESSON A
13
GAIN OR GAIN + COST
COST OR FALSE CLAIM
Less effort: gain
Pull down: direction benefit
Slower + stronger turn: both
Farther hand travel: cost
Extra energy created: false
Notes: We Do 2 — 3 minutes within the source's 40-minute lesson.
Next three minutes. Source bins classify false energy claim as NEITHER. Explain gears' 'stronger turn' means greater turning effect/torque, not energy creation. For lever, compare same load and rise before claiming easier. Invite pupil to move/draw model showing both outcomes.
[Sources]
https://github.com/MattRoper1977/Lessons/blob/main/Science_Teesside/Grow/SCI_G_W4_Mechanisms.html
Git blob: 8aa3e1f001c3d3c944207d4eb44b93b1df4d7e46.
SHA256: a2d4bd4b2ec87aace94167b285bd1724bb9e2907f86a472b74b84fa48ffa53a0.
[/Sources]

## Slide 14
MADE BY MATT / GROW SCIENCE
Keep both halves of the explanation
AUTUMN 1 · WEEK 4 · LESSON A
14
Moving the pivot nearer the load can reduce the effort force needed.
For the same small load rise, the effort end must travel farther.
EFFORT
LOAD
PIVOT
Notes: We Do 2 — 2 minutes within the source's 40-minute lesson.
Final two minutes of source We Do 2. No mechanism creates energy; real mechanisms also dissipate some. Stop Monday here, label and keep work. Tuesday uses 32-minute lever comparison, 4-minute feedback and 4-minute exit. Do not add practical or exit today.
[Sources]
https://github.com/MattRoper1977/Lessons/blob/main/Science_Teesside/Grow/SCI_G_W4_Mechanisms.html
Git blob: 8aa3e1f001c3d3c944207d4eb44b93b1df4d7e46.
SHA256: a2d4bd4b2ec87aace94167b285bd1724bb9e2907f86a472b74b84fa48ffa53a0.
[/Sources]